## Slide 1
IETF 105 Side Meeting: Trustworthy Multipurpose Remote ID (tm-rid)
Extending Locator/Identifier split & strong authentication techniques to identify physically nearby objects
Bob Moskowitz, Stu Card, Adam Wiethuechter

## Slide 2: Remote ID / V2X Applications
Remote ID itself as an app (vs enabling technology)
Platform
  Command & Control
  Detect And Avoid (DAA) “self separation”
  Collision Avoidance
Payload
  Mission apps, e.g. remote sensing

## Slide 3: Aerial Internet Weaknesses
Today’s Internet has significant weaknesses in
  Mobility
  Multicast
  Multihoming
  Management
  Quality of Service
  Security
Aero wireless networking compounds these…

## Slide 4: Some network issues compounded by aeronautical communications
Each non-trivial aircraft has multiple radios of different types
Many types of radios hand off between base stations frequently
Most open standard protocols are challenged by
  Low data rates
  High error (or loss) rates
  Long latencies
  Link asymmetry
  Rapid wide variation in channel characteristics
Security protocols requiring cryptographic handshakes are further challenged by
  Limited on-board processing power
  Brief contact time w/fast moving platforms
Enormous safety implications (e.g. remotely crash my drone).
Aggregation of enough public information enables inference of sensitive information about the physical world (e.g. air operations routes & schedules).

## Slide 5: 1st Mitigation: Multiple Wireless Links
Aviation authorities will require at least 2 largely independent radio systems for reliability
Multiple links also greatly benefit security
  jammer must jam all your links to deny you service
  info can be spread over N links so an eavesdropper must listen on at least M of them to learn anything
3 links are obvious in many cases today
  WiFi or other RF LOS coverage built to suit
  LTE, w/extensive coverage already built out
  Iridium or other global coverage systems
End systems & users
  Should know what network Quality of Service they currently can expect
  But should not need to know which link[s] reach a given UA at a given time

## Slide 6: 2nd Mitigation: Strong ID Based Security
Aircraft identity is distinct from its physical (spatial) & logical (network) locations
  Aircraft identifiers should be distinct from locators (e.g. current IP addresses)
  Security associations should belong to identity, not location, thus remain unaffected by handoff between radio base stations
IETF Host Identity Protocol (HIP) offers
  identifier / locator de-conflation as justified above
  identifiers corresponding to crypto public keys
  IPSEC interoperability w/automatic dynamic setup
  multi-homing (multiple concurrent network connections)
  smooth make-before-break handoff between base stations

## Slide 7: Cyber Resilient Communications
Demonstrated maintaining control of UAS w/HIP-based robust/secure C2.
Assured C2 over multiple links (WiFi & LTE) w/automatic failover/fallback.
Strongly encrypted communications between authenticated endpoints w/persistent IDs.

## Slide 8: HIP benefits for Remote ID
General
  Give each device a persistent identifier that remains the same across IP address changes
    enable persistent TCP connections, security associations, etc.
  Give all packets a provenance
    “Secure Mobile Architecture” (Boeing, Lockheed-Martin, et al)
    see R. Paine’s Beyond HIP: The End to Hacking As We Know It
  Auto-configure IPsec VPNs (frustrating to do manually)
Aero networking
  Associate persistent identifier with aircraft tail #
  Multihoming for make-before-break smooth handoff

## Slide 9
Broadcast Remote ID
One-way transmissions
  UAS to observer devices w/RID app
Short range media
  Bluetooth 4.X beacon & 5 extended advertisement
  Wifi w/Neighbor Awareness Networking (NAN)

## Slide 10
Network Remote ID (Net-RID)
Uses various Internet media
  Typically LTE
Net-RID Service Provider (SP)
  Gather data from connected UASes & other sources
Net-RID Display Provider (DP)
  Connection point for RID APP
  Aggregate data that user requests for a given area
SP & DP can be co-located or remote to each other
UAS Service Supplier is expected to be SP only or both

## Slide 11
Using HIP for RID
Broadcast RID
  Trustworthy (verifiable) persistent ID using HIT
Network RID
  Can leverage all of HIP advantages
    Persistent ID of all interconnected devices (UAS, USS)
    Automagic IPSec ESP tunnels

## Slide 12
Strawman ODID Auth Message
Interval start timestamp
Interval end timestamp
Hash of previous Auth Message
Hash of current Auth Message (0 when computing)?
Hashes of all other messages sent during interval
Signature using HIT private key

## Slide 13
Proposed Next Steps
Propose ASTM add HIP HIT as an ID Type
  already talking w/ASTM & FAA
Define any necessary HIP extensions
  already drafting ODID Auth Message
Extend Open Drone ID implementation
Integrate HIP into USS (Net-ID DP/SP)